## Slide 1: MPLS TE
Antonio Virdis
Assistant Professor@ University of Pisa
antonio.virdis@unipi.it
Notes: http://www.ciscopress.com/articles/printerfriendly/426640

## Slide 2: MPLS TE
Traditional IP networks uses destination-based routing
Explicit routing (e.g. source based routing) is not supported
MPLS networks can support destination-based and explicit routing simultaneously
TE is a generic name corresponding to the use of different technologies to optimize the utilization of a given backbone capacity and topology.
MPLS TE uses extensions to RSVP and MPLS forwarding to support constrained-based routing (taking into account more information on network constraints and policy requirements)
Notes: TE is a generic name corresponding to the use of different technologies to optimize the utilization of a given backbone capacity and topology.

## Slide 3: MPLS TE
Resource optimization, avoid over- and under- utilization of network parts, traffic not being aggregated on the shortest path

## Slide 4: Configuration Steps
prerequisites
CEF and tagswitch on every interface
Enable tunnel creation
Enable TE in IGP
Create tunnel(s)

## Slide 5: OSPF configuration
RIP is a distance vector routing protocol, only link-state routing protocols that provide constant updates on the link state can be used
For this reason we need to configure OSPF (already done in the MPLS scenario)
  router ospf 100
  network 10.1.1.0 0.0.0.3 area 1
  network 10.2.2.0 0.0.0.3 area 1
  network 192.168.1.0 0.0.0.255 area 1
  network 192.168.2.0 0.0.0.255 area 1
  network 192.168.3.0 0.0.0.255 area 1
as seen from R1

## Slide 6: Loopback configuration
It is mandatory to setup a Loopback interface with IP mask of 32 bits on each router to be used as router-id
  interface Loopback0
  ip address 172.16.1.1 255.255.255.255
  router ospf 100
  network 172.16.1.1 0.0.0.0 area 1
Notes: Configure a loopback interface for tunnel association to the TE tunnel

## Slide 7: MPLS
Cisco MPLS implementation requires CEF – Cisco Express Forwarding
CEF is an advanced layer 3 switching technology adopted in cisco routers to increase packet switching speed
CEF keeps track of adjacencies to build the Forwarding Information Base (FIB)

## Slide 8: MPLS Configuration
Configugre
  ip cef
    Enable CEF
  interface Serial 2/0
    mpls ip
      Enable tag switching on this interface
Check
  show mpls interfaces detail
Notes: Additional ref:
https://www.cisco.com/c/en/us/support/docs/multiprotocol-label-switching-mpls/mpls/13731-mpls-te-ospf.html

## Slide 9: Test
Open Wireshark and try to ping VoipServer from VoipClient
Notes: if you look at the connection R1-R2, you should see MPLS header only for ping requests (client->server), and not for ping responses. This is due to the Penultimate Hop Popping.

## Slide 11: Test
show mpls forwarding table

## Slide 12: MPLS - TE
Unlike conventional IP routing MPLS traffic engineering (TE) uses the implicit MPLS characteristic of separation between the forwarding plane and the control plane to allow routing decisions to be made on criteria other than the destination address
Label switched paths (LSPs), referred as “traffic engineering tunnels” are setup to steer traffic through the network allowing links not included in the shortest path to be used

## Slide 13: MPLS TE - enable Tunnels
Enable the creation of mpls tunnels for TE:
  mpls traffic-eng tunnels
    Enable tunnels creation on the router
  Interface serial 2/0
  mpls traffic-eng tunnels
  ip rsvp bandwidth 512 512
    Enable MPLS tunnel creation on the interface specifying the reservable bandwidth and the largest reservable flow on the interface
Enable TE extension on OSPF
  router ospf 100
    mpls traffic-eng area 1
    mpls traffic-eng router-id Loopback0
RSVP adopted also as admission control
Notes: why two “mpls traffic-eng tunnels” commands? The first one enables tunneling at the router level (global), the second one does it at the itnerface level.

## Slide 14: MPLS TE - Tunnels
Define a new (headend) tunnel:
  interface Tunnel0
  ip unnumbered Loopback0
  tunnel destination 172.16.1.5
  tunnel mode mpls traffic-eng
  tunnel mpls traffic-eng autoroute announce
  tunnel mpls traffic-eng priority 2 2
  tunnel mpls traffic-eng bandwidth 400
  tunnel mpls traffic-eng path-option 1 dynamic
    The path of the tunnel will be dynamically selected
Check the status:
  show mpls traffic-eng tunnels
Reservation priority for the tunnel
Notes: By default, the tunnel interface is not announced into the IGP for use in the routing table. This will have to be configured explicitly for the tunnel interface to be used as the next hop in the routing table by the IGP.
This configuration has to be performed at the ingress of the tunnel (R1)
To check reachability show mpls traffic-eng topology path destination xxx.xxx.xxx.xxx

## Slide 15: Having “fun” with show commands
show mpls interface detail
﻿show mpls traffic-eng tunnels
﻿show mpls traffic-eng topology
show mpls traffic-eng topology path destination xxx.xxx.x.x
﻿show mpls traffic-eng link-management igp-neighbors
﻿show mpls traffic-eng link-management interfaces
﻿show mpls traffic-eng link-management statistics
show ip route
Notes: Configure R1 and R2. Partially configure R5 “forgetting” to include -mpls traffic-eng tunnels- in the interface configuration.
Then search the “bug” through show commands:
show mpls traffic-eng tunnels on R1: the tunnel is not working
show mpls traffic-eng topology path destination xxx.xxx.x.x: from R1 to R2 and vice-versa will work. Towards R5 will fail instead
show mpls interface detail on R5: notice tunneling is disabled.
Fix it
show mpls traffic-eng topology on R1: show the correct resource allocation on R1 and R2

## Slide 16
interface serial 2/1
shutdown
Notes: We already have a tunnel between R1 and R5, allocating 400 Kbps
We now shutdown interface s2/0 of R1 (to avoid using the lower part of the network).
We then try to install a new tunnel between R1 and R5, requesting 400 kbps, and having priority 3 3

## Slide 17: MPLS TE – Dynamic Tunnels
Define a tunnel (headend) with dynamic path:
  interface Tunnel01
  ip unnumbered Loopback1
  tunnel destination 172.16.1.5
  tunnel mode mpls traffic-eng
  tunnel mpls traffic-eng autoroute announce
  tunnel mpls traffic-eng priority 5 5
  tunnel mpls traffic-eng bandwidth 400
  tunnel mpls traffic-eng path-option 1 dynamic
setup & hold
priorities
Check tunnel status
  ﻿show mpls traffic-eng tunnels brief
Notes: This configuration has to be performed at the ingress of the tunnel (R1)
A tunnel interface can have several path options, to be tried successively

## Slide 18: MPLS TE – Dynamic Tunnels (2)
Tunnel0
Tunnel1
Setup
Hold
Setup
Hold

## Slide 19: Differentiate routing
To differentiate routing you can set static routes (e.g. for load balancing):
  ip route 192.168.101.0 255.255.255.0 Tunnel0
  ip route 192.168.102.0 255.255.255.0 Tunnel01
192.168.101.0
192.168.102.0
Tunnel0
Tunnel1
Notes: This configuration has to be performed at the ingress of the tunnel (R1)

## Slide 20: Test 1
Generate tunnel0 (priority 2 2)
Generate tunnel01 (priority 3 3)
Turn on serial 2/1 on R1
Increase priority of tunnel01 to 1 1
Check tunnel status at each step
Observe traffic

## Slide 21: MPLS TE – Explicit-path Tunnels
Define a tunnel (headend) with explicit path:
  interface Tunnel1
      ip unnumbered Loopback0
      tunnel destination 172.16.1.5
      tunnel mode mpls traffic-eng
      tunnel mpls traffic-eng autoroute announce
      tunnel mpls traffic-eng priority 2 2
      tunnel mpls traffic-eng bandwidth 400
      tunnel mpls traffic-eng path-option 1 explicit name longpath
      tunnel mpls traffic-eng path-option 2 dynamic bandwidth 400
tunnel mpls traffic-eng path-option 3 dynamic bandwidth 0
Define the path:
  ip explicit-path name longpath enable
    next-address 10.2.2.2
    next-address 10.3.3.2
    next-address 10.4.4.2
Notes: This configuration has to be performed at the ingress of the tunnel (R1)
A tunnel interface can have several path options, to be tried successively

## Slide 22
      tunnel mpls traffic-eng path-option 1 explicit name longpath
      tunnel mpls traffic-eng path-option 2 dynamic bandwidth 400
tunnel mpls traffic-eng path-option 3 dynamic bandwidth 0

## Slide 23: Test 2
Remove either tunnel0 or tunnel01
Create tunnel1
Check where traffic is going

## Slide 24: Test 2
show ip route

## Slide 25: Test 2
RSVP messages can be seen

## Slide 26: Test 2
Open Wireshark on one of the links in the long path and try to ping a Server from a Client
Response is sent on the short path!

## Slide 27: Path protection
Notes: https://www.cisco.com/c/en/us/td/docs/ios-xml/ios/mp_te_path_protect/configuration/xe-3s/mp-te-path-protect-xe-3s-book/mp-te-path-prot.html#:~:text=Glossary%20Close-,MPLS%20Traffic%20Engineering%20(TE)%20Path%20Protection,traffic%20engineering%20(TE)%20tunnels.

## Slide 28: Path protection (2)
interface tunnel2
…
tunnel mpls traffic-eng path-option 1 explicit name shortpath
tunnel mpls traffic-eng path-option protect 10 explicit name longpath
  ip explicit-path name shortpath enable
    next-address 10.1.1.2
    next-address 10.5.5.2

## Slide 29: Test 3
Create a tunnel between R1 and R5
Use an explicit path R1-R2-R5 as primary
Use an explicit path R1-R3-R4-R5 as secondary
Observe traffic
Shutdown any interface of R2
Observe traffic again